## Slide 1
TRANSLATION STAGE CONTROL
For EvWaCo Prototype
Present by Nunnalin Auephattanaphong (Internship)
Robotics Engineering and AI, CMU.

## Slide 2
ABOUT INTERNSHIP PROJECT
Get to know instruments
Error Measurement Method
1
2
3
4
Agenda
5
Experiment & Application
Conclusion

## Slide 3
01
About Internship project
1

## Slide 4
2
Translation stage control project is a mini project that part of Evanescent Wave Coronagraph (EvWaCo) prototype project from NARIT.
Evanescent Wave Coronagraph or EvWaCo is a type of Lyot coronograph that aim to develop optical instruments for collect the starlight and companion light.
The main idea of translation stage control project is
Introduction
control translation stage moving along horizontal axis for moving light source
to make the light source closest align
Notes: control translation stage moving light source along horizontal axis to make the light source closest align to imaging system for get high quality image by using PID closed loop control .

## Slide 5
3
Why we use PID Control ?
Stability and Responsiveness : The D term dampens oscillations, while the I term corrects steady-state errors, leading to a more stable system.
Improved Accuracy : The I term ensures the system output matches the desired setpoint more precisely.
Flexibility : PID provides three tunable parameters (Kp, Ki, Kd) to optimize performance for different systems and dynamic behaviors.
In summary, PID control offers balanced error management, enhancing stability, accuracy, and responsiveness over pure error control.

## Slide 6
PID CONTROLLER
Stands for “Proportional, Integral, Derivative” .
It is closed-loop feedback control .
instrument used by control engineers to regulate temperature, flow, pressure, speed, and other process variables in industrial control systems.
https://microcontrollerslab.com/pid-controller-implementation-using-arduino/
4

## Slide 7
PID CONTROLLER
tuning -> correcting a target proportional to the difference
tuning -> cumulating the error result from the “P” action to increase the correction factor
tuning -> minimize overshoot by slowing the correction factor
based on the current error ( setpoint - measured output of the system )
Increase the contribution of the accumulated error over time to the control signal
reduce the rate of change of the error
P : Proportional
I : Integral
D : Derivative
helps improve the stability and responsiveness of the control loop
5

## Slide 8
PID CONTROLLER
P Controller
Use only error term to affect the output
simply multiply error with the gain constant
provides a linear relationship between the error of a system and the controller output of the system
6
Relation between PID Output and error (e(t))
P,I,D term
mm
t
t
t
Translation stage position
error
Kp * e(t)

## Slide 9
PID CONTROLLER
PI Controller
a combination of Proportional controller action and Integral controller action
correlates the controller output to the error and the integral of the error.
provides a faster response time than
I-only control
Eliminates steady state error
7

## Slide 10
PID CONTROLLER
PD Controller
combination of feedforward and feedback control
contains - proportional control’s damping
of the fluctuation
  - derivative control’s prediction
  of process error output
Improves transient response, reduces overshoot
8
error

## Slide 11
PID CONTROLLER
PID Controller
a combination of all three types of control methods
most commonly used
balances steady state and transient response
9

## Slide 12
02
Get to know instruments
10

## Slide 13
11
chrome-extension://efaidnbmnnnibpcajpcglclefindmkaj/https://optomechs.com/pdf/manuals/KDC101/KDC101_ManualforKinesis.pdf
https://telescopes.net/zwo-asi1600mm-pro-monochrome-cmos-camera.html
https://www.thorlabs.com/thorproduct.cfm?partnumber=DDS100/M
INSTRUMENTS
KDC101 -> Controller for control DDS100/M
DDS100/m -> One axis translation Stage
ASI1600mm PRO -> Camera for capture images
Mainly focus on
KDC101
DDS100/M
ASI1600mm PRO
Optical components
Light source
Mirrors
lens

## Slide 14
12
SETUP
Schematic
ASI1600mm-PRO
Reference Light source
Translation stage with light source
Lens
Lens
Lens
Lens
Mirror

## Slide 15
Moving translation stage into steps for find error of stage .
Home position can’t change.
Home position is 0.0000 .
1. Find error of translation stage
13
Error of translation stage is 0.0100 – 0.0500 .

## Slide 16
Try capture some image from ASI1600-PRO Camera and save images into .jpg for MONO8 and .tiff file. For MONO16
https://www.tecnosky.eu/index.php/zwo-asi-1600mm-pro-usb-3-0-cooled-mono.html
2. Capture image from camera
14

## Slide 17
03
Error Measurement Method
15

## Slide 18
WORKFLOW
16
START
Capture reference image
Capture image
Find error distance between 2 circles
PID CONTROL
FINISH
Circles close to reference ?
Yes
No
Mainly focus on
Find distance between 2 circles
Find solution for overlapped circles condition
Normalized pixels to millimeters
Notes: Flowchart

## Slide 19
OVERVIEW MAP
17

## Slide 20
2. Find distance between 2 circle by
1.Find coordinate of center of 2 circles
2.Subtrac coordinate of center of 2 circles
METHOD 1
3. Find center coordinates and distance of circle
18
1. Find center coordinates of circle by
Use Matplotlib for plot circle.
Using OpenCV for find edge , contour area and coordinate of center point.

## Slide 21
Can’t use this condition with image that has 2 circles that are overlapping
METHOD 1
3. Find center coordinates and distance of circle
19

## Slide 22
Coding program for draw and plot circles from circle formula .
Initialize as 2D array .
Plot histogram for see intensity of circle
METHOD 2
3. Find center coordinates and distance of circle
20
This code works for overlapped circle condition .
Can’t find distance between 2 images.

## Slide 23
AND
XOR
Main idea of this concept is
Use bitwise operation (AND , XOR) for find contour area that not overlapping. Then draw bounding box around the area then find height and width then calculate center of the area from height and width. Then find distance between 2 center point.
METHOD 3
3. Find center coordinates and distance of circle
21
Notes: บอกว่าใช้method3 ในการใช้จริง

## Slide 24
METHOD 3
3. Find center coordinates and distance of circle
22
Notes: Using image that collected from lab for testing method 3

## Slide 25
METHODS | ADVANTAGES | DISADVANTAGES
Contour area | Easy for operate | Can’t use this method with overlapped images
Histogram plot | Can use this method with overlapped images | Can’t find distance between 2 images.
Bitwise operation | Can use this method with overlapped images | Take more time to process
23

## Slide 26
Normalized data from pixel to mm.
24

## Slide 27
04
Experiment & Application
25

## Slide 28
EXPERIMENT
Test code in lab with method 3 as solution for collect real data and find possible issue when run in the actual setup .
26

## Slide 29
Solution
Find centroid and position of dot both in reference image and collected image.
PROBLEM : Have only one light source
so it can’t see 2 dot in one image at the same time.
Compare position of current image with reference image.
Problem and solution 1
EXPERIMENT
27
(Still use bitwise operation method in code for overlapped condition)

## Slide 30
Solution : Coding new program that has infinite loop to read current images .
PROBLEM : Program doesn’t read current images that had capture . It’s read and overwrite old images in directory instead .
Problem and solution 2
EXPERIMENT
28

## Slide 31
Problem and solution 3
EXPERIMENT
29
PROBLEM : Program read and draw wrong contour area . It’s read the random tiny pixels instead of the real reference pixels . So, it’s effect to calculate distance between current pixels and reference pixels.
Solution : Select and draw the biggest contour as reference pixels .

## Slide 32
Application have 2 versions
30
UI Version
Command line Version

## Slide 33
Application
Command line version for users.
31

## Slide 34
Application
Have 2 options .
32
Option 1 : Enter values with default values.
Option 2 : Enter values with other values.
First version of UI version

## Slide 35
Collected feedback from users
33
Add the title of application
Display properly dynamic range of PID parameters
Create Stop and Home button
Initialize the PID parameters in entry boxes
Short describe for effect of each PID parameters

## Slide 36
34
Current Version of application for users
Title of application
Short description about PID parameters
Initialized (Default)
PID parameters
Add stop button
Add Home button

## Slide 37
35
Add alert Window for notify when put some values that out of range.
The dynamic range of values is in README.md file

## Slide 38
05
Conclusion
36

## Slide 39
Block Diagram
Reference
PID
Translation
stage
Image
Processing
Camera
Σ
Control translation stage with PID control
Find method for get error to calculate PID
Some graph doesn’t see difference between PID parameters enough because some of algorithm. Develop algorithm in the future
Idea for develop in the future
Achievement
37

## Slide 40
38
Default values of PID are :
P : Proportional : 10
I : Integral : 0.1
D : Derivative : 0.2
Initial position : 60
Application can work with the same PID values for difference reference position from different reference image .
Reference position = 53.37
Reference position = 55.48
Relation between translation stage position and setpoint
mm
Relation between translation stage position and setpoint
mm

## Slide 41
Both UI version and input command in terminal version work successfully.
Can control translation stage with PID closed loop control and collect images.
39
UI Version
Command line Version

## Slide 42
THANK YOU
40
Reference position = 55.48